## Slide 1: LiDAR Processing and Target Identification – Changepoint Detection MSU ECE REU Site Summer 2022 Final Project Presentation
Presenter: Caroline Xu
Mentor: Dr. Brad Whitaker
Co-authors: Trevor Vannoy, Nat Sweeney, Ryan Ficken

## Slide 2: Introduction
Entomologists want to study insect behavior using LiDAR
  Agriculture
  Species conservation
Inefficient to manually look through images
Use machine learning techniques to automate process to speed up insect identification

## Slide 3: Research Question
How can we use changepoint detection to create an unsupervised machine learning algorithm to detect insects in LiDAR images?
Can we use changepoint detection as an alternative to supervised machine learning methods?

## Slide 4: LiDAR
Light Detection And Radar
Shoots laser out and receives a return signal when it hits something
6kHz-8kHz pulse frequency
Beam is ~5 cm in diameter
Trevor Vannoy, MSU, 2022

## Slide 5: Changepoint Detection
Type of unsupervised learning: figures out differences by itself
Looks at changes in data
Mean
Variance/Standard Deviation
Notes: explain why use mean and how it actually works

## Slide 6: Data Collection
Hyalite Creek (2020)
  09/16 – 09/18, 09/20
  10,079 images
MSU Honey Bee Research Site and Pollinator Garden (2022)
  06/23 – 06/24
  4132 images
Images are 178x1024 pixels
  178 range bins ~ 0.5 m
  1024 pulses → ~ 128-170 milliseconds
  Images used are normalized to values 0 - 1
Joe Shaw and Trevor Vannoy, MSU, 2022

## Slide 7: Methodology
Find ways to preprocess the data
Use processed data and input into changepoint functions
Look at results
  Runtime
  Accuracy
Adjust code as necessary to improve performance
Repeat

## Slide 8: Methodology
Preprocess Data
Input Processed Data into Changepoint Detection Functions
Adjust Code to Improve Performance
Look at Results
(Runtime and Accuracy)
Apply Algorithm on New Data
Is Performance Satisfactory?
Yes
No
Repeat

## Slide 9: Preprocessing

## Slide 10: Preprocessing (Row Removal)
Removed Empty Rows

## Slide 11: Preprocessing (Row Removal)
Removed Hard Targets

## Slide 12: Preprocessing (Row Removal)
Removed Rows With No Change

## Slide 13: Preprocessing (Row Removal)
Removed Rows With No Frequency
(no change)
Notes: Explain that removing rows did not remove insects for Hyalite, can assume same for bee dataset

## Slide 14: Preprocessing (Wavelet Transform)
Continuous Wavelet Transform (cwt) Scalogram
Cropped, Processed, and Normalized Scalogram

## Slide 15: Preprocessing (Wavelet Transform)
Average of Each Column in Normalized Scalogram
Smoothed and Normalized Signal

## Slide 16: Changepoint Functions
Changepoint Detection on Smoothed Scalogram Signal
Changepoint Detection on Original Signal

## Slide 17: Post Processing
Identify insect position using mean of signal between each changepoint
  Can look at position of each insect instead of entire image
Remove insects that were too short or too long
  < 15 pixels or > 700 pixels
Plot column in insect position to check for maximum value at correct row

## Slide 18: Post Processing
Examine Row Signal
Not Enough Change
Examine Insect Length
< 15 or > 700
Plot Column
Peak Doesn't Match Row
Peak Matches Row
Enough Change
Length Between 15 & 700

## Slide 19: Algorithms
Insect Algorithm
Bee Algorithm
Minimum threshold for changepoints were 3.9 and 3
  Less sensitivity means only confident on significant signals
Minimum of 15 pixels, maximum of 605 pixels
  Not as many long insect signals in Hyalite dataset
Did not plot columns
Minimum threshold for changepoints were 2 and 0.8
  Increased sensitivity means more changepoints
Minimum of 15 pixels, maximum of 700 pixels
  Long signals more common in bee dataset
Plotted columns

## Slide 20: Hyalite Dataset Results
Used insect algorithm
Runtime of 4 hours for 10079 images
97.6% accuracy
Identified 71.1% of all insects
195 false positives
  2% of all images without insects were falsely identified to have insects

## Slide 21: Bee Dataset Results
Used bee algorithm
Runtime of 2 hours 15 minutes for 4132 images
73.3% accuracy
Identified 65.5% of all insects
651 false positives
  23.1% of all images without insects were falsely identified to have insects

## Slide 22: Bee Dataset Results
Used insect algorithm
Runtime of 2 hours 50 minutes for 4132 images
81.4% accuracy
Identified 51.3% of all insects
132 false positives
  4.7% of all images without insects were falsely identified to have insects

## Slide 23: Analysis
It took 5 hours 5 minutes to run both algorithms on the bee data linearly
It took 35 hours to manually label all of the bee images taken over the course of two days
  Split between 5 people
  Took 5 days to complete

## Slide 24: Analysis
Insect algorithm does not perform as well as it looks
  Less insects and more images in the dataset
  False positives and false negatives have smaller impact
  More false positives than actual positives
Algorithms on bee dataset can be improved
  Less false positives than actual positives
  Still missing a lot of insect images

## Slide 25: Analysis
Mainly caught the prominent signals
  Weak or noisy signals could not be identified
Because of wavelet transform, bright DC signals within the insect signal did not show up in scalogram
  No frequency detected
Performance still not ideal
  Too many false positives; decent results by chance?
Signals seen in data might not be insects
  No way to verify

## Slide 26: Analysis
Variety of insect signals
Nearly impossible to create perfect algorithm

## Slide 27: Conclusions
Changepoint detection can be a viable replacement to supervised machine learning
  Greatly reduces time to go through all the images
  Relatively accurate
Future Directions:
Improve accuracy and runtime of models
  Use voltage matrix instead of normalized matrix
  Find faster way to reduce rows
  Run everything in parallel instead of linearly
Pinpoint reason behind false negatives and false positives
Look at other changepoint detection functions like gfpop[1]
[1] Hocking, T. D., Rigaill, G., Fearnhead, P., & Bourque, G., "Generalized functional pruning optimal partitioning (gfpop) for constrained changepoint detection in genomic data," arXiv, 2018.

## Slide 28: Broader Impacts
Technical:
Changepoint detection can be used instead of supervised ML in similar scenarios (drone detection, etc.)
Personal:
Learned a lot about signal processing and gained experience with unsupervised ML and field tests
Learn more about grad school as a future option
Go back to school and look for research to do
Apply engineering thinking skills to project teams and school

## Slide 29: Acknowledgements
Dr. Brad Whitaker
  Project Mentor
Dr. Kevin Repasky and Dr. Wataru Nakagawa
  Principal Investigator (PI) and Co-PI
Trevor Vannoy
  Graduate Student Behind the Research Project
Dr. Joe Shaw
  Built the insect LiDAR
Nat Sweeney
  Changepoint Detection Buddy
ECE REU Students
Thank you!